## Slide 1
Computer Architecture
By
Dr.Hadi Hassan
Integer Multiplication and Division

## Slide 2
Paper and Pencil Example:
Multiplicand 11002 = 12
Multiplier × 11012 = 13
1100
0000
1100
1100
Product 100111002 = 156
m-bit multiplicand × n-bit multiplier = (m+n)-bit product
Accomplished via shifting and addition
Consumes more time and more chip area than addition
Binary multiplication is easy
0 × multiplicand = 0
1 × multiplicand = multiplicand
Unsigned Multiplication

## Slide 3
Initialize Product = 0
For each iteration ,check the first bit of the Multiplier
If Multiplier bit = 1 then Product = Product + Multiplicand
Shift the multiplier to right and multiplicand to the left
The product of multiplication of 32-bit register by 32-bit register is ≤ 64 bits.
Evolution of Multiplication Algorithms
First version of multiplication:

## Slide 4
Control decides when to
Shift the Multiplicand and Multiplier.
When to write new values into the Prod.
Multiplication Hardware
At each bit we need to have the following operations:
Product=Product+Multiplicand.
Shift Multiplicand left.
Shift Multiplier right.
If each of the above operation requires one clock cycle, we need 96 cycles to multiply two 32-bit registers (3x32=96).
Initially 0
00001100
00000000
00000000
00001100
1101
00001100
1
110
0
00011000
00011000
00001100
00001100
11
00110000
00110000
00001100
1
00111100
1
1
01100000
01100000
00111100
10011100

## Slide 5
$Mcand=0110; $Mplier=0101; $Prod= 00011110 |  |  |  | 
Iteration | Step | $Mplier | $Mcand | $Product
0 | initial | 0101 | 0000 0110 | 0000 0000
1 | a. $Mplier0= 1; $Prod=$Prod+$Mcand b. $Mplier (Shift Right) c.$Mcand ( Shift left ) | ------ 0010 ------- | ---- ---- ---- ---- 0000 1100 | 0000 0110 0000 0110 ---- ---- ----- -----
 | End of iteration 1 | 0010 | 0000 1100 | 0000 0110
2 | a.$Mplier0= 0; no operation b. $Mplier (Shift Right) c.$Mcand ( Shift left ) | ----- 0001 ----- | ---- ---- ---- ---- 0001 1000 | 
 | End of iteration 2 | 0001 | 0001 1000 | 0000 0110
3 | a. $Mplier0= 1; $Prod=$Prod+$Mcand b. $Mplier (Shift Right) c.$Mcand ( Shift left ) | ----- 0000 | ---- ---- ---- ---- 0011 0000 | 0001 1000 0001 1110 ---- ---- ---- ----
 | End of iteration 3 | 0000 | 0011 0000 | 0001 1110
4 | a.$Mplier0= 0; no operation b. $Mplier (Shift Right) c.$Mcand ( Shift left ) | ------- 0000 ----- | -------------- --------------- 0110 0000 | 
END | End of iteration 4 | 0000 | 0110 0000 | 0001 1110

## Slide 6
Optimized Multiplier
Instead of shifting Multiplicand and product . The
digits of the two number will be the same.
2. Second Version of Multiplication

## Slide 7
Registers needed for
  multiplicand
  multiplier
  product
Use lower 32 bits of product register:
  place multiplier in lower 32 bits
  add multiplicand to higher 32 bits
  product = product >> 1
  repeat
Critique

## Slide 8
Version 1 versus Version 2

## Slide 9
$Mcand=0110; $Mplier=0101; $Prod= 00011110 |  |  |  | 
Iteration | Step | $Mplier | $Mcand | $Product
0 | initial | 0101 | 0110 | 0000 0000
1 | a. $Mplier0= 1; (L.H )$Prod=(L.H)$Prod+$Mcand b. $Mplier (Shift Right) C $Prod ( Shift Right ) | ------ 0010 ------- | ------- ---- ---- ------- | 0110 0110 0000 ---- ---- 0011 0000
 | End of iteration 1 | 0010 | 0110 | 0011 0000
2 | a.$Mplier0= 0; no operation b. $Mplier (Shift Right) C $Prod ( Shift Right ) | ----- 0001 ----- | ---- ---- ---- ---- --------- | 0001 1000
 | End of iteration 2 | 0001 | 0110 | 0001 1000
3 | a. $Mplier0= 1; (L.H )$Prod=(L.H)$Prod+$Mcand b. $Mplier (Shift Right) c.$Mcand ( Shift Right ) | ----- 0000 | ---- ---- ---- ---- -------- | 0110 0111 1000 ------------- 0011 1100
 | End of iteration 3 | 0000 | 0110 | 0011 1100
4 | a.$Mplier0= 0; no operation b. $Mplier (Shift Right) c.$Prod ( Shift Right ) | ------- 0000 ----- | ------------ ------------ ------------- | -------- -------- --------- -------- 0001 1110
END | End of iteration 4 | 0000 | 0110 | 0001 1110

## Slide 10
Since both $prod and $Mplier are shifted right, and the L.H. $prod is 0’s at initial state, the $Mplier can be loaded in the right half of the $prod. This eliminates the $Mplier register, and therefore simplify the hardware.
3. Third Version of Multiplication
Multiplier (shifts right)

## Slide 11
$Mcand=0110; $Mplier=0101; $Prod= 00011110 |  |  |  | 
Iteration | Step |  | $Mcand | $Product
0 | initial |  | 0110 | 0000 0101
1 | a. $Mplier0= 1; (L.H )$Prod=(L.H)$Prod+$Mcand b. $Prod ( Shift Right ) |  | ------- ---- ---- ------- | 0110 0110 0101 ---- ---- 0011 0010
 | End of iteration 1 |  | 0110 | 0011 0010
2 | a.$Mplier0= 0; no operation b. $Prod ( Shift Right ) |  | ---- ---- ---- ---- --------- | ------- -------- 0001 1001
 | End of iteration 2 |  | 0110 | 0001 1001
3 | a. $Mplier0= 1; (L.H )$Prod=(L.H)$Prod+$Mcand b.$Prod ( Shift Right ) |  | ---- ---- ---- ---- -------- | 0110 0111 1001 ---- ---- 0011 1100
 | End of iteration 3 |  | 0110 | 0011 1100
4 | a.$Mplier0= 0; no operation b.$Prod ( Shift Right ) |  | ------------ ------------ ------------- | -------- -------- --------- -------- 0001 1110
END | End of iteration 4 |  | 0110 | 0001 1110

## Slide 12
Signed Multiplication
So far, we have dealt with unsigned integer multiplication
First Attempt:
  Convert multiplier and multiplicand into positive numbers
    If negative then obtain the 2's complement and remember the sign
  Perform unsigned multiplication
  Compute the sign of the product
  If product sign < 0 then obtain the 2's complement of the product
Better Version:
  Use the unsigned multiplication hardware
  When shifting right, extend the sign of the product
  If multiplier is negative, the last step should be a subtract

## Slide 13
Signed Multiplication (Pencil & Paper)
Case 1: Positive Multiplier
Multiplicand 11002 = -4
Multiplier × 01012 = +5
11111100
111100
Product 111011002 = -20
Case 2: Negative Multiplier
Multiplicand 11002 = -4
Multiplier × 11012 = -3
11111100
111100
00100 (2's complement of 1100)
Product 000011002 = +12
Sign-extension
Sign-extension

## Slide 14
ALU produces 32-bit result + Sign bit
Check for overflow
  No overflow  Extend sign-bit of result
  Overflow  Invert extended sign bit
Sequential Signed Multiplier
= 0
Start
LO[0]?
First 31 iterations: HI = HI + Multiplicand
Last iteration: HI = HI – Multiplicand
32nd Repetition?
Done
= 1
No
Yes
HI = 0, LO = Multiplier
Shift Right (Sign, HI, LO) 1 bit
32-bit ALU
Control
64 bits
32 bits
write
add, sub
LO[0]
Multiplicand
shift right
32 bits
HI
LO
32 bits
sign

## Slide 15
Signed Multiplication Example
Consider: 11002 (-4) × 11012 (-3), Product = 000011002
Check for overflow: No overflow  Extend sign bit
Last iteration: add 2's complement of Multiplicand
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 0 1 1 0 0 1
LO[0] = 0 => Do Nothing
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 1 1 0 0 1 1
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 1 0 0 1 1 0
Shift (Sign, HI, LO) right 1 bit
0 0 0 0 1 1 0 0
2
1 1 0 0
0 0 0 0 1 1 0 1
Initialize (HI = 0, LO = Multiplier)
0
1
3
4
Multiplicand
Product = HI, LO
Sign
Iteration
1
1 1 0 0 1 1 0 1
LO[0] = 1 => ADD
+
1
1 0 1 1 0 0 1 1
LO[0] = 1 => ADD
+
0 1 0 0
0
0 0 0 1 1 0 0 1
LO[0] = 1 => SUB (ADD 2's compl)
+
= 0
Start
LO[0]?
First 31 iterations: HI = HI + Multiplicand
Last iteration: HI = HI – Multiplicand
32nd Repetition?
Done
= 1
No
Yes
HI = 0, LO = Multiplier
Shift Right (Sign, HI, LO) 1 bit

## Slide 16: The Booth Multiplier
Booth algorithm is an elegant way to multiply signed numbers using same hardware as before and save cycles
Observation: if we can both add and subtract, there are multiple ways to create a product
Example: multiply 2ten by 6ten (0010two X 0110two)
  Product = (2 X 2) + (2 X 4) OR
  Product = (2 X -2) + (2 X 8)
  6=-2+8 0110 = – 00010 + 01000 = 11110 + 01000
0010
X 0110
+ 0000 shift
+ 0010 shift + add
+ 0010 shift + add
+ 0000 shift
00001100
Regular Algorithm
0010
X 0110
0000 shift
- 0010 shift + subtract
0000 shift
+ 0010 shift + add
00001100
Booth’s Algorithm

## Slide 17
0
1
1
0
0
1
1
1
0
0
Beginning
Of Run
Middle
Of Run
End
Of Run
Bit ai
Bit ai-1
Explanation
1
0
Begin Run of 1’s
1
1
Middle of Run of 1’s
0
1
End of Run
0
0
Middle of Run of 0’s
Scan multiplier bits from right to left
Test 2 bits of multiplier at once
  “Current” bit ai
  Bit to right of “current” bit ai-1
Multiplicand
(32 bits)
Product (64 bits)
Write
Control
32-bit ALU
Shift Left
ADD/ SUB
2
Bits 1:0
LHPROD
(32 bits)
MP/RHPROD (32 bits)
Implementing Booth’s Algorithm
Key idea: test 2 bits of multiplier at once
  10 - subtract (beginning of run of 1’s)
  01 - add (end of run of 1’s)
  00, 11 - do nothing (middle of run of 0’s or 1’s)

## Slide 18
Operation Multiplicand Product next?
0. initial value 0010 0000 0111 0 10 -> sub
1a. P = P - m 1110 + 1110 1110 0111 0 shift P (sign ext)
1b. 0010 1111 0011 1 11 -> nop, shift
2. 0010 1111 1001 1 11 -> nop, shift
3. 0010 1111 1100 1 01 -> add
4a. 0010 + 0010
0001 1100 1 shift
4b. 0010 0000 1110 0 done
Booths Example (2 x 7)

## Slide 19
Booths Example (2 x -3)
1a. P = P - m 1110 + 1110 1110 1101 0 shift P (sign ext)
1b. 0010 1111 0110 1 01 -> add + 0010
2a. 0001 0110 1 shift P
2b. 0010 0000 1011 0 10 -> sub + 1110
3a. 0010 1110 1011 0 shift
3b. 0010 1111 0101 1 11 -> nop
4a 1111 0101 1 shift
4b. 0010 1111 1010 1 done
Operation Multiplicand Product next?
0. initial value 0010 0000 1101 0 10 -> sub

## Slide 20
Iteration | Mcand | Step | Product
0 | 0010 | Initial values | 0000 0110,0
1 | 0010 0010 | 00: no op arith>> 1 | 0000 0110,0 0000 0011,0
2 | 0010 0010 | 10: prod-=Mcand arith>> 1 | 1110 0011,0 1111 0001,1
3 | 0010 0010 | 11: no op arith>> 1 | 1111 0001,1 1111 1000,1
4 | 0010 0010 | 01: prod+=Mcand arith>> 1 | 0001 1000,1 0000 1100,0
Booths Example (2 x 6)

## Slide 21
MIPS Instructions
mult $s2, $s3 computes the product and stores
it in two “internal” registers that
can be referred to as hi and lo
mfhi $s0 moves the value in hi into $s0
mflo $s1 moves the value in lo into $s1
Similarly for multu

## Slide 22
Try to see how big a number can be subtracted, creating a digit of the quotient on each attempt
= 19 Quotient
Divisor 10112 110110012 = 217 Dividend
-1011
10
101
1010
10100
-1011
1001
10011
-1011
10002 = 8 Remainder
Unsigned Division (Paper & Pencil)
Binary division is accomplished via shifting and subtraction
Dividend =
Quotient × Divisor
+ Remainder
217 = 19 × 11 + 8
1
0
0
1
12

## Slide 23
Division
1001ten Quotient
Divisor 1000ten | 1001010ten Dividend
-1000
10
101
1010
-1000
10ten Remainder
At every step,
  shift divisor right and compare it with current dividend
  if divisor is larger, shift 0 as the next bit of the quotient
  if divisor is smaller, subtract to get new dividend and shift 1 as the next bit of the quotient
Unsigned Division (Paper & Pencil)

## Slide 24
1001ten Quotient
Divisor 1000ten | 1001010ten Dividend
0001001010 0001001010 0000001010 0000001010
100000000000  0001000000 00001000000000001000
Quo: 0 000001 0000010 000001001
At every step,
  shift divisor right and compare it with current dividend
  if divisor is larger, shift 0 as the next bit of the quotient
  if divisor is smaller, subtract to get new dividend and shift 1 as the next bit of the quotient
Unsigned Division (Paper & Pencil)

## Slide 25
Sequential Division
Uses two registers: HI and LO
Initialize: HI = Remainder = 0 and LO = Dividend
Shift (HI, LO) LEFT by 1 bit (also Shift Quotient LEFT)
  Shift the remainder and dividend registers together LEFT
  Has the same net effect of shifting the divisor RIGHT
Compute: Difference = Remainder – Divisor
If (Difference ≥ 0) then
  Remainder = Difference
  Set Least significant Bit of (Lo) Quotient
Observation to Reduce Hardware:
  LO register can be also used to store the computed Quotient

## Slide 26
Sequential Division Hardware
Initialize:
  HI = 0, LO = Dividend
Results:
  HI = Remainder
  LO = Quotient
Start
Difference?
2. HI = Remainder = Difference
Set least significant bit of LO
32nd Repetition?
Done
< 0
≥ 0
No
Yes
Shift (HI, LO) Left
Difference = HI – Divisor
shift left
Divisor
32-bit ALU
LO
32 bits
write
sub
32 bits
Difference
sign
set lsb
HI
32 bits
Control

## Slide 27
Division Example
Example: 11102 / 00112 (4-bit dividend & divisor)
Result Quotient = 01002 and Remainder = 00102
4-bit registers for Remainder and Divisor (4-bit ALU)
2: Diff < 0 => Do Nothing
2: Rem = Diff, set lsb of LO
1 0 0 1
0 0 0 0
2: Diff < 0 => Do Nothing
2: Diff < 0 => Do Nothing
2
0 0 0 0
1 1 1 0
Initialize
0
1
3
4
HI
Difference
LO
Iteration
0 0 1 1
Divisor
1 1 1 0
1: Shift Left, Diff = HI - Divisor
0 0 0 1
1 1 0 0
0 0 1 1
0 0 0 0
1: Shift Left, Diff = HI - Divisor
0 0 1 1
1 0 0 0
0 0 1 1
1 1 1 0
1: Shift Left, Diff = HI - Divisor
0 0 0 1
0 0 1 0
0 0 1 1
1 1 1 1
1: Shift Left, Diff = HI - Divisor
0 0 1 0
0 1 0 0
0 0 1 1
Start
Difference?
2. HI = Remainder = Difference
Set least significant bit of LO
32nd Repetition?
Done
< 0
≥ 0
No
Yes
Shift (HI, LO) Left
Difference = HI – Divisor

## Slide 28
Divide Example
Divide 7ten (0111two) by 2ten (0010two)
Iter | Step | Hi | L0 | Divisor | Difference
0 | Initial values | 0000 | 0111 | 0010 | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
Start
Difference?
2. HI = Remainder = Difference
Set least significant bit of LO
32nd Repetition?
Done
< 0
≥ 0
No
Yes
Shift (HI, LO) Left
Difference = HI – Divisor

## Slide 29
Signed Division
Simplest way is to remember the signs
Convert the dividend and divisor to positive
  Obtain the 2's complement if they are negative
Do the unsigned division
Compute the signs of the quotient and remainder
  Quotient sign = Dividend sign XOR Divisor sign
  Remainder sign = Dividend sign
Negate the quotient and remainder if their sign is negative
  Obtain the 2's complement to convert them to negative

## Slide 30
Signed Division Examples
Positive Dividend and Positive Divisor
  Example: +17 / +3 Quotient = +5 Remainder = +2
Positive Dividend and Negative Divisor
  Example: +17 / –3 Quotient = –5 Remainder = +2
Negative Dividend and Positive Divisor
  Example: –17 / +3 Quotient = –5 Remainder = –2
Negative Dividend and Negative Divisor
  Example: –17 / –3 Quotient = +5 Remainder = –2
The following equation must always hold:
Dividend = Quotient × Divisor + Remainder